## Slide 1
Cryogenic Safety Awareness
Module version: 1.2
Contact Safety Training at ESS:
Safety Training Service Desk
Safety Training on Confluence

## Slide 2: Objectives of the course
Know about cryogenic fluids and the related risks
Be able to recognise a potential hazard
Know the correct behaviour to adopt in the event of an emergency
1.
3.
2.
The aim of this e-learning course is to raise your awareness or remind you of important information about cryogenic hazards, the various related risks and the responsibilities and expected behaviour of everyone accessing the ESS site, particularly premises and facilities that contain cryogenic installations and/or equipment. As for any other risk, ESS endeavours to take all the necessary actions to reduce and manage cryogenic hazards, including training you to be the principal actor in matters of safety.
After completing this course, you will:

## Slide 3: Cryogenic Safety
Instructions
    Please turn on the sound

## Slide 4: Cryogenic Safety
6. Game
3. Emergency
4. Prevention and Protection
5. Further Information
1. Basics
2. Hazards
Course chapters

## Slide 5
1. Basics

## Slide 6: Basics
Cryogenic fluids at ESS
HOME
Cryogenics is the study of the production and behaviour of materials at very low temperatures.
Cryogenic fluids are widely used at ESS:
In the accelerator, cryogenics cool the Superconducting Radio Frequency cavity cryomodules to their 2 K operation point.
In the target, cryogenics provides the nominal 15 K cooling needed for the supercritical hydrogen moderator.
In the area of neutron science, liquid helium is supplied for use in sample environment systems and in superconducting magnets of some instruments.
The most common gases used at ESS that can exist as cryogens are: helium, nitrogen and argon.
At room temperature cryogenic fluids are gases. At extremely low temperatures they are in a liquid state.

## Slide 7: Basics
Cryogenic range of temperatures
Ar
18
Argon
He
2
Helium
N2
7
Nitrogen
4.2
87.3
K
77.3
0
Absolute
zero
Click on to reveal the
Celsius and Fahrenheit values
Kelvin [K] is the unit of measurement for temperature, based upon an absolute scale. Its null point (absolute zero) is the lower limit of the thermodynamic temperature scale.
ESS cavities: 2 K = -271.15 °C = -456.07 °F

## Slide 8: Basics
Cryogenic range of temperatures
Absolute
zero
18
Argon
He
2
Helium
N2
7
Nitrogen
4.2
K
0
Absolute Zero:
-273.15°C
-452.11 °F
Ar
87.3
77.3
Click on to reveal the
Celsius and Fahrenheit values
Kelvin [K] is the unit of measurement for temperature, based upon an absolute scale. Its null point (absolute zero) is the lower limit of the thermodynamic temperature scale.
ESS cavities: 2 K = -271.15 °C = -456.07 °F

## Slide 9: Basics
Cryogenic range of temperatures
Absolute
zero
18
Argon
He
2
Helium
N2
7
Nitrogen
4.2
K
0
Ar
Liquid Argon:
-185.85 °C
-302.53 °F
87.3
77.3
Click on to reveal the
Celsius and Fahrenheit values
Kelvin [K] is the unit of measurement for temperature, based upon an absolute scale. Its null point (absolute zero) is the lower limit of the thermodynamic temperature scale.
ESS cavities: 2 K = -271.15 °C = -456.07 °F

## Slide 10: Basics
Cryogenic range of temperatures
Absolute
zero
18
Argon
He
2
Helium
N2
7
Nitrogen
Liquid Helium:
-269 °C
-452.11 °F
4.2
K
0
Ar
87.3
77.3
Click on to reveal the
Celsius and Fahrenheit values
Kelvin [K] is the unit of measurement for temperature, based upon an absolute scale. Its null point (absolute zero) is the lower limit of the thermodynamic temperature scale.
ESS cavities: 2 K = -271.15 °C = -456.07 °F

## Slide 11: Basics
Cryogenic range of temperatures
Absolute
zero
18
Argon
He
2
Helium
N2
7
Nitrogen
Liquid Nitrogen:
-195.85 °C
-320.53 °F
4.2
K
0
Ar
87.3
77.3
Click on to reveal the
Celsius and Fahrenheit values
Kelvin [K] is the unit of measurement for temperature, based upon an absolute scale. Its null point (absolute zero) is the lower limit of the thermodynamic temperature scale.
ESS cavities: 2 K = -271.15 °C = -456.07 °F

## Slide 12: Basics
He
2
Helium
Absolute
zero
18
Argon
N2
7
Nitrogen
Cryogenic vs daily life range of temperatures
HO
Freezing pt.
2
HO
Boiling pt.
2
Room
Temp.
373.15
293.15
273.15
0
Ar
Click on to reveal the
Celsius and Fahrenheit values
0
Cryogenic
Range
123
K

## Slide 13: Basics
He
2
Helium
Absolute
zero
18
Argon
N2
7
Nitrogen
Cryogenic vs daily life range of temperatures
HO
2
Room
Temp.
Room Temp.:
~ 20 °C
68 °F
373.15
293.15
273.15
0
Freezing pt.
HO
Boiling pt.
2
Ar
Click on to reveal the
Celsius and Fahrenheit values
0
Cryogenic
Range
123
K

## Slide 14: Basics
He
2
Helium
Absolute
zero
18
Argon
N2
7
Nitrogen
Cryogenic vs daily life range of temperatures
HO
2
HO
Boiling pt.
2
Room
Temp.
373.15
293.15
273.15
0
Freezing pt.
Water freezing pt:
0 °C
32 °F
Ar
Click on to reveal the
Celsius and Fahrenheit values
0
Cryogenic
Range
123
K

## Slide 15: Basics
He
2
Helium
Absolute
zero
18
Argon
N2
7
Nitrogen
Cryogenic vs daily life range of temperatures
HO
2
HO
Boiling pt.
2
Room
Temp.
Water boiling pt:
100 °C
212 °F
373.15
293.15
273.15
Freezing pt.
Ar
0
Click on to reveal the
Celsius and Fahrenheit values
0
Cryogenic
Range
123
K

## Slide 16: Basics
Cryogenic fluid behaviour
Helium
Argon
Nitrogen
Click on to reveal the behaviour of the cryogenic fluids

## Slide 17: Basics
Cryogenic fluid behaviour
Helium
Argon
Nitrogen
Helium is lighter than air, so will rise
He

## Slide 18: Basics
Cryogenic fluid behaviour
Helium
Argon
Nitrogen
Cold nitrogen is heavier than air, so will accumulate at floor level
N2

## Slide 19: Basics
Cryogenic fluid behaviour
Helium
Argon
Nitrogen
Argon is heavier than air, so will accumulate at floor level
Ar

## Slide 20: Basics
Cryogenic fluid behaviour
Helium
All elements, including cryogens, expand when evaporating from liquid to gas.
Argon
Nitrogen
HOME

## Slide 21
2. Hazards

## Slide 22: Hazards
Signage
Cold surfaces
Oxygen Deficiency Hazard (ODH)
Pressure release
The following warning signs indicate:

## Slide 23: Hazards
Cryogenic-related hazards: physical
There are two classes of hazards related to cryogenics: physical and physiological.
Physical hazards include:
Rupture of the equipment or a part of it due to the excessive pressures that cryogenic fluids may reach.
Damage to or deterioration of the equipment, as a result of materials not suitable for cryogenics, becoming brittle due to the extremely low temperatures
Oxygen enrichment around cold surfaces: oxygen from the air may condense, forming droplets that could cause and/or accelerate a fire.
HOME

## Slide 24: Hazards
Cryogenic-related hazards: physiological
The physiological hazards relate to potential health effects.
Touching a cryogenic fluid or a cold surface may cause:
Contact burns: blister-like burns
Frostbite: our skin freezes, resulting in permanent damage and discoloration
Inhaling cold vapour can cause permanent damage to the lungs and may lead to asphyxiation.
In either case, exposure of a few seconds could be enough to cause damage!

## Slide 25: Hazards
Cryogenic-related hazards: oxygen deficiency
The air we breathe is a mixture of oxygen (21%) and nitrogen (78%). In the event of a cryogenic release, the liquid will evaporate rapidly, displacing the breathable air and thus creating an oxygen deficiency hazard (ODH). Oxygen deficiency can lead to…
Oxygen Level vs Physiological Effects
21%
Normal, safe oxygen levels
18%
ESS ODH Alarm
threshold
Fast breathing,
drowsiness, nausea
15%
5-0 %
Unconsciousness
Death
12-10%

## Slide 26: Hazards
Cryogenic-related hazards
If you come across a tanker refilling a cryogenic tank, avoid getting close to it! The danger should be indicated and the area fenced off.
HOME
CRYO TRANSFER

## Slide 27
3. Emergency

## Slide 28: Emergency
Cryogen releases can occur due to overpressure in the equipment, which may be caused by human error or by heat loads exceeding standard operating conditions.
How to recognise an emergency situation
Liquid or gaseous cryogens used at ESS are odourless, colourless and tasteless. The white cloud observed during a cryogen release is water vapour condensing in the ambient air, but it is no longer visible when the gas warms up.
WATER
CLOUD
indicate cold surfaces
might indicate a leak of liquid or gaseous cryogens
RUSHING GAS
NOISE OF
ICE
OR
OR
OR
HOME
CONDENSATION
AIR

## Slide 29: Emergency
How to react: flashing lights, vapour cloud, noise
If you see flashing lights or a vapour cloud, or if you hear the noise of rushing gas: LEAVE THE AREA IMMEDIATELY!
Evacuate calmly away from the flashing light and the cryogenic fluid leak (vapour cloud, noise), following the escape routes indicated by the green signs.
DO NOT WALK INTO THE VAPOUR CLOUD!

## Slide 30: Emergency
How to react: you find yourself in a vapour cloud
If you find yourself in a vapour cloud
Hold your breath and get out of the cloud, walking towards the nearest safe exit. The vapour might be cold and could damage your lungs if inhaled.

## Slide 31: Emergency
REMEMBER: argon and cold nitrogen are heavier than air, so you should stand up as the oxygen concentration will be higher further up.
How to react: you find yourself in a vapour cloud
Ar/N2
He
He
REMEMBER: helium is lighter than air, so you should crouch down as the oxygen concentration will be higher at floor level.

## Slide 32: Emergency
You hear the evacuation alarm but you don’t see a flashing light or a vapour cloud and you can’t hear the noise of rushing gas
How to react: you hear the evacuation alarm
Evacuate calmly to the nearest safe exit, but if you see flashing lights or a vapour cloud or hear the noise of rushing gas while you are walking, change direction!
REMEMBER: the evacuation alarm could have been triggered by another emergency, such as a fire

## Slide 33: Emergency
If you see someone lying on the floor but there is no vapour cloud or any other sign of an emergency situation…
… it doesn’t mean that there is no emergency. The gas might have reached room temperature so that you can’t see the cloud anymore. The oxygen concentration could have decreased, causing the victim to lose consciousness.
Call the Emergency Rescue Service on 112
How to react: you see someone lying on the floor
PREV
PREV
NEXT
It could be dangerous for you as well. Do not put your life at risk if there is an ODH alarm.

## Slide 34: Emergency
In all cases
Alarm
When you have reached a safe place, call the Emergency Rescue Service on 112 to report the emergency. If you hear a message asking you to wait, hold the line until they take your call!
IN ALL CASES: leave the area immediately and activate the nearest alarm on the evacuation route.

## Slide 35: Emergency
In all cases
HOME
AFTER THE ACCIDENT: don’t forget to complete an Internal Accident Report form in BIA (Project username: ESS – Password: Power14) to report any damage to ESS’ property or the environment, or injuries to people on the ESS site.
Once outside, go to the nearest assembly point and wait for the arrival of the Emergency Rescue Service. DO NOT LEAVE THE AREA WITHOUT THE EMERGENCY RESCUE SERVICE’S AUTHORISATION: they will need to check that everyone has safely evacuated the premises!

## Slide 36
4. Prevention

## Slide 37: Prevention and Protection
Best practice and behaviour
You should:
keep a safe distance from cryogenic installations
identify and locate the hazards indicated by the different signs
avoid contact with cryogenic fluids
REMEMBER that damaged insulation can expose extremely cold surfaces, which are not always obviously recognisable, and if condensation or ice appear on the surface of cryogenic equipment, avoid skin contact. If you have any doubt, ask the Installation owner.
You must respect alarms and signage and adapt your behaviour accordingly
HOME

## Slide 38
5. Further Information

## Slide 39: Further Information
HOME
HOME
Any activity/area/equipment at ESS involving the use of asphyxiant fluids that could have an impact on people’s safety shall be compliant with the ESS guideline for Oxygen Deficiency Hazard.
Contact Safety Training at ESS:
Safety Training Service Desk
Safety Training on Confluence

## Slide 40: Game
Each of the three doors will take you to a different scenario, where you will have to make decisions and answer questions. This is not the final test, but it’s good training for it.
You can go through as many of the doors as you like, it’s up to you.
Have fun!
HOME

## Slide 41: Game
Choose one of the doors by clicking on a key
SCENARIO 1
SCENARIO 2
SCENARIO 3
EXIT

## Slide 42: Scenario 1
You work in an environment presenting cryogenic hazards…
What does the sign
below mean?
Risk of falling asleep
Oxygen Deficiency Hazard

## Slide 43: Scenario 1
You work in an environment presenting cryogenic hazards…
What does the sign
below mean?
Risk of falling asleep
Oxygen Deficiency Hazard

## Slide 44: Scenario 1
You work in an environment presenting cryogenic hazards…
Oops! Try again
Seriously?

## Slide 45: Scenario 1
You work in an environment presenting cryogenic hazards…
Well done!
If the oxygen concentration falls below 12-10 % you will lose consciousness

## Slide 46: Scenario 1
You are walking towards your office…
… when you hear the evacuation alarm…
… There are no signs of an emergency…
Nothing, there is no real emergency
I activate the alarm
I evacuate the area
What do you do?

## Slide 47: Scenario 1
You are walking towards your office…
… when you hear the evacuation alarm…
… There are no signs of an emergency…
Nothing, there is no real emergency
I activate the alarm
I evacuate the area
What do you do?

## Slide 48: Scenario 1
You are walking towards your office…
… when you hear the evacuation alarm…
… There are no signs of an emergency…
Well done!
Even if you don’t see any signs of an emergency, something must have triggered the alarm

## Slide 49: Scenario 1
You are walking towards your office…
… when you hear the evacuation alarm…
… There are no signs of an emergency…
Oops! Try again
Even if you don’t see any signs of an emergency, something must have triggered the alarm!

## Slide 50: Scenario 1
You are walking towards your office…
… when you hear the evacuation alarm…
… There are no signs of an emergency…
Oops! Try again
The alarm is already sounding!

## Slide 51: Scenario 1
As you are leaving the area, you notice someone lying on the floor in another room
PREV
PREV
NEXT
What do you do?
I continue to evacuate
I enter the room

## Slide 52: Scenario 1
PREV
PREV
NEXT
You faint. What happened?
I am in shock
There was probably a cryogenic release and the oxygen level is below 12%.

## Slide 53: Scenario 1
PREV
PREV
NEXT
PREV
PREV
NEXT
You faint. What happened?
I am in shock
There was probably a cryogenic release and the oxygen level is below 12%.

## Slide 54: Scenario 1
PREV
PREV
NEXT
PREV
PREV
NEXT
Correct
You have put yourself in danger too!

## Slide 55: Scenario 1
PREV
PREV
NEXT
PREV
PREV
NEXT
Oops! Try again
This is a possibility, but it’s more likely that you didn’t see the cloud because it had reached room temperature, so the right answer is…

## Slide 56: Scenario 1
You continue to evacuate…
PREV
PREV
NEXT
PREV
PREV
NEXT
I go to the assembly point and wait.
I call the Emergency Rescue Service
Both answers are correct
What do you do
next?

## Slide 57: Scenario 1
You continue to evacuate…
PREV
PREV
NEXT
PREV
PREV
NEXT
I go to the assembly point and wait.
I call the Emergency Rescue Service
Both answers are correct
What do you do
next?

## Slide 58: Scenario 1
You keep evacuating…
PREV
PREV
NEXT
PREV
PREV
NEXT
Correct…
… but what else?

## Slide 59: Scenario 1
You keep evacuating…
PREV
PREV
NEXT
PREV
PREV
NEXT
Well done!
I call the Emergency Rescue Service to let them know there’s a victim who needs to be rescued. I also go to the assembly point and wait for the Emergency Rescue Service’s authorisation to leave.
.

## Slide 60: Scenario 1
You’re outside, safe. REMEMBER: DO NOT LEAVE THE AREA WITHOUT THE EMERGENCY RESCUE SERVICE’S AUTHORISATION! They need to confirm that everyone has safely evacuated the premises!
PREV

## Slide 62: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Argon
Cold nitrogen
Helium
The cloud is rising. Which cryogen acts like this?

## Slide 63: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Argon
Cold nitrogen
Helium
The cloud is rising. Which cryogen acts like this?

## Slide 64: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Well done!
Helium is lighter than air

## Slide 65: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Oops! Try again
Cold nitrogen is heavier than air

## Slide 66: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Oops! Try again
Argon is heavier than air

## Slide 67: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
What is the best thing to do in this situation?
Crouch down
Stand up

## Slide 68: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Well done!
It’s helium, so oxygen concentration is higher at floor level

## Slide 69: Scenario 2
You are in your work environment, when you see a cloud coming out of a cryogenic vessel…
Oops! Try again
It’s helium: oxygen concentration is higher at floor level!

## Slide 70: Scenario 2
The cloud starts expanding…
What could happen if you inhaled the cold gas?
Nothing: it’s just water condensation
It might damage my lungs

## Slide 71: Scenario 2
The cloud starts expanding…
What could happen if you inhaled the cold gas?
Nothing: it’s just water condensation
It might damage my lungs

## Slide 72: Scenario 2
The cloud starts expanding…
Oops! Try again
It is water condensation, but it is mixed with gas at very low temperature!

## Slide 73: Scenario 2
The cloud starts expanding…
Well done!
And it could also cause asphyxiation

## Slide 74: Scenario 2
You must evacuate!
What should you do before leaving the building?
I activate the evacuation alarm
I check if there is anyone left in the building

## Slide 75: Scenario 2
What should you do before leaving the building?
I activate the evacuation alarm
I check if there is anyone left in the building

## Slide 76: Scenario 2
Oops! Try again
You shouldn’t go back, it’s too dangerous now!

## Slide 77: Scenario 2
Well done!
You activate the alarm, and once you are safe you should call the Emergency Rescue Service
and explain the situation to them

## Slide 78: Scenario 2
911
115
112
What is the Emergency Rescue Service’s
number?

## Slide 79: Scenario 2
911
115
112
What is the Emergency Rescue Service’s
number?

## Slide 80: Scenario 2
Oops! Try again
You should never forget the correct number!

## Slide 81: Scenario 2
Well done!
Always remember this number!

## Slide 82: Scenario 2
DO NOT LEAVE THE AREA WITHOUT THE EMERGENCY RESCUE SERVICE’S AUTHORISATION! They need to confirm that everyone has safely evacuated the premises!
PREV

## Slide 84: Scenario 3
You see droplets coming from the surface of a cryogenic pipe…
Helium
What could these droplets be?
Air condensation
Water

## Slide 85: Scenario 3
You see droplets coming from the surface of a cryogenic pipe…
Helium
What could these droplets be?
Air condensation
Water

## Slide 86: Scenario 3
You see droplets coming from the surface of a cryogenic pipe…
Helium
Oops! Try again
Not everything that looks like water is water…

## Slide 87: Scenario 3
You see droplets coming from the surface of a cryogenic pipe…
Helium
Well done!
Air condensation might be due to bad insulation

## Slide 88: Scenario 3
This is a dangerous situation…
In addition, you notice that the droplets are falling onto a bin full of paper…
Helium
What is the risk now?
Surface burn, similar to frostbite
Fire

## Slide 89: Scenario 3
In addition, you notice that the droplets are falling onto a bin full of paper…
This is a dangerous situation…
Helium
What is the risk now?
Surface burn, similar to frostbite
Fire

## Slide 90: Scenario 3
In addition, you notice that the droplets are falling onto a bin full of paper…
This is a dangerous situation…
Helium
Not really, try again!
Only if you come in contact with the cryogen. Remember the general rule: I don’t know, I don’t touch!

## Slide 91: Scenario 3
In addition, you notice that the droplets are falling onto a bin full of paper…
This is a dangerous situation…
Helium
Well done!
The oxygen in the air condenses, causing the droplets to form. Since oxygen concentration increases, this could result in a fire

## Slide 92: Scenario 3
You have to do something!
Helium
What do you do?
Contact the equipment owner
Cover the bin

## Slide 93: Scenario 3
You have to do something!
Helium
What do you do?
Contact the equipment owner
Cover the bin

## Slide 94: Scenario 3
You have to do something!
Helium
Oops! Try again
If your skin gets in contact with the droplets you may get frostbite. You will also be close to a potential fire source.

## Slide 95: Scenario 3
You have to do something!
Helium
Well done!
He or she is the responsible for the equipment and will know what to do!

## Slide 96: Scenario 3
Helium
Call the equipment owner to explain the situation…
You just contributed to making ESS safer.
PREV
He or she will cordon off the area and repair the insulation
Improve Safety at ESS even more: once you are back in your office, complete an Internal Accident Report form in BIA.